## Slide 1: Introduction to Networking
CS 241
April 16, 2014
University of Illinois

## Slide 2: Announcements
Last call for Pebble pickup
  Right after class today

## Slide 3: Networking
What do we expect out of networking?
  An channel between two processes on two remote machines.
Making this happen is complex!
Hosts
Routers
Various Links
Applications
Protocols
Hardware
Software
Bit errors
Packet errors
Link failures
Node failures
Message delays
Out-of-order delivery
Eavesdropping
Host
Proc
Host
Proc
Ex: Firefox on your machine
Ex: Facebook’s server

## Slide 4: Protocols
A protocol is a message format and rules for exchanging these messages.
You already use a lot of protocols:
Notes: Web / Http
ssh
SNMP / email

## Slide 5: What is a Protocol?
Human protocols
  “what’s the time?”
  “I have a question”
  Introductions
Network protocols
  Machines rather than humans
  All Internet communication is governed by protocols
Hi
Hi
Got the
time?
2:00
TCP connection
request
TCP connection
response
Get http://www.uiuc.edu
<file>
time

## Slide 6: Networking Model: Layers of Protocols
A network channel is effectively only a transmission of 0s and 1s:
How do we translate these 0s and 1s into HTTP packets? How do we get those to the right end-user?
0 1 0 0 1 1 0 1 0 0 0 1 0 1 1 0 0 1 0 1 1 1 1 0 1 0
Host
Proc
Host
Proc

## Slide 7: The Internet’s Protocol Stack
The Internet’s core protocols form a “stack”.
  Larger seven-layer stack devised by a committee in the 1980s is called the OSI Model
  Here we focus on layers commonly used today
Each layer encapsulates data sent by the layers above it and provides specific features to higher-layer protocols.
Physical
Data Link
Network
Transport
Application

## Slide 8: Layer 1: Physical Layer
The Physical Layer provides hardware-specific details on how to transmit a 0 vs. 1.
  100BASE-T: Ethernet
  GSM “Um Interface”: Cell phones
  802.11: Wi-Fi
Provides: A digital representation of the underlying signal; a series of 0s and 1s.
Key problem: Analog to digital conversion
Physical
Data Link
Network
Transport
Application
Notes: So basically we’re dealing with physics. What are some of the physical media we operate over?
Air (radio), light in glass fiber, copper cables

## Slide 9: Physical transmission media
[Photos: Wikimedia users Evdaimon, Zephyris, BigRiz]

## Slide 10: Physical transmission media
[Wikimedia user Timwether]

## Slide 11: Layer 2: Data Link Layer
The Data Link Layer sends and receives packets on a transmission medium.
  Consider Wi-Fi:
    Every computer that is connected to a wi-fi access point uses the same channel: every computer hears every other computer!
    How do we know the data that is coming in is for us, not for our neighbor?
Provides: Send/receive packets on a “wire”
Key problems:
  Framing, errors
  Addressing, resource contention
Physical
Data Link
Network
Transport
Application
Notes: Run ifconfig, talk about MAC addresses

## Slide 12: Layer 2: Data Link Layer
Network Node
Network Node
Network Node
Packet:
Data Link Packet
Payload
Packet:
New data link layer between every link!
…but the “payload” remains the same.
Layer 2 Header
Data Link Packet
Payload
Layer 2 Header

## Slide 13: Layer 3: Network Layer
The Network Layer provides host-to-host communications across many “hops”.
  One protocol: IP (IPv4 and IPv6)
Provides: Information on the source and destination host.
  Where should this packet go?
  Who sent this packet in the first place?
Key problems:
  Addressing
  Heterogeneous transmission media
  Routing
Physical
Data Link
Network
Transport
Application
Notes: Traceroute demo?

## Slide 14: Layer 4: Transport Layer
The Transport Layer provides process-to-process communications.
  Two main protocols: TCP and UDP
Provides: Information on the source and destination process… and much more.
  Uses “network ports”, a globally shared resource on a system that associates a port number with a process.
  The process making the connection to a remote process needs to know the port number the remote process is listening on.
Key problems:
  Process multiplexing, reliability, congestion...
Physical
Data Link
Network
Transport
Application

## Slide 15: TCP vs. UDP
TCP and UDP both provide process-to-process communications via port numbers.
  That is about all UDP does. UDP: fast and cheap!
TCP provides several convenience features:
  Reliable Transmission:
    Packets will arrive in the order that they were sent
    All packets will arrive (on an active connection)
    All packets will be delivered once (no duplicates)
  Flow and Congestion Control:
    TCP negotiates a rate of transmission between the hosts so the receiver is not overwhelmed with data

## Slide 16: Application Layer (“layer 7”)
The Application Layer refers to any communication software and procedures for particular applications.
  May actually be composed of many layers
Examples?
Physical
Data Link
Network
Transport
Application

## Slide 17: Where are we as systems programmers?
Most commonly, we write applications using an interface to the transport layer
  In this class: the sockets interface
  Others exist
Above sockets interface: User code
Below sockets interface: Kernel
Physical
Data Link
Network
Transport
Application

## Slide 18: Encapsulation
Application
program
Application
program
Application
program
Reliable
Service
Host-to-Host
DATA
IP HDR
DATA
Application
program
Reliable
Service
Host-to-Host
DATA
TCP HDR
DATA
TCP HDR
IP HDR
DATA
Best effort
Service
Best effort
Service
TCP HDR
IP HDR
DATA
TCP HDR
IP HDR
DATA

## Slide 19: Why layering?
It’s all about modularity
  Eases maintenance, updating of system
  Change of implementation of layer’s service transparent to rest of system
  e.g., change in transmission medium (Layer 0) has no effect on network protocol or applications
What other examples of layering have we seen?

## Slide 20: Internet Architecture: The “Hourglass” Design
FTP
TCP
Modem
MPLS
3G wireless
Ethernet
IP
UDP
TFTP
NV
HTTP