## Slide 1: Networking wrap-up and I/O systems
CS 241
April 28, 2014
University of Illinois
Notes: Didn’t make it to the I/O part at all.
Need to put the review questions into a SurveyMonkey ... forgot to do that :-(

## Slide 2: Today
Network programming tips
Network Address Translation
I/O systems

## Slide 3: Tip #1: Can’t bind?
Problem: bind() says “address already in use”
  You have stopped your server, and then re-started it right away
  The sockets that were used by the first incarnation of the server are still active

## Slide 4: setsockopt
int yes = 1;
setsockopt (fd, SOL_SOCKET, SO_REUSEADDR,
(char *) &yes, sizeof (yes));
  Call just before bind()
  Allows bind to succeed despite the existence of existing connections in the requested TCP port
  Connections in limbo (e.g. lost final ACK) will cause bind to fail

## Slide 5: Tip #2: Dealing with abruptly closed connection
Notes: Show main loop of ./37-server.c
Have client connect via telnet, then exit (control-] and type ‘quit’).
What does the server do?
Fix by uncommenting signal line in ./37-server.c.

## Slide 6: Tip #2: Dealing with abruptly closed connection
Problem: Socket at other end is closed
  Write to your end generates SIGPIPE
  This signal kills the program by default!
signal (SIGPIPE, SIG_IGN);
  Call at start of main in server
  Allows you to ignore broken pipe signals
  Can ignore or install a proper signal handler
  Default handler exits (terminates process)

## Slide 7: Tip #3: Beej’s guide
Beej's Guide to Network Programming
http://beej.us/guide/bgnet/

## Slide 8: Review

## Slide 9: Threads in your web server
Why are multiple threads useful in your web server – as opposed to serving all clients with a single thread in a single process? (Check all that apply)
  Multiple threads can spread work across multiple cores / CPUs to decrease processing time.
  Multiple threads have greater memory space to read files and write them to the network.
  A single thread would have to switch back and forth between each connection, which is slow and annoying to program.
  One thread can be reading/writing from the network while another is waiting to read a file off disk.

## Slide 10: DNS caching
Why does the DNS system use caching? (Check all that apply)
  Returns more up-to-date results
  Improves speed of response
  Decreases workload on root and authoritative DNS servers
  Improves security
  Improves robustness (things still work even if some DNS servers fail)

## Slide 11: Network Address Translation (NAT)

## Slide 12: The problem
Your ISP gives you one IP address. But...

## Slide 13: NAT: Network Address Translation
Approach
  Assign one router a global IP address
  Assign internal hosts local IP addresses
  A box in the middle converts between them
    (e.g. wireless router in your home)
When a packet arrives from the Internet, how do you know which internal host it’s destined for?

## Slide 14: NAT: Network Address Translation
10.0.0.1
10.0.0.2
10.0.0.3
S: 10.0.0.1, 3345
D: 128.119.40.186, 80
1
10.0.0.4
138.76.29.7
1: host 10.0.0.1
sends datagram to
128.119.40, 80
NAT translation table
WAN side addr LAN side addr
138.76.29.7, 5001 10.0.0.1, 3345
…… ……
S: 128.119.40.186, 80
D: 10.0.0.1, 3345
4
S: 138.76.29.7, 5001
D: 128.119.40.186, 80
2
2: NAT router
changes datagram
source addr from
10.0.0.1, 3345 to
138.76.29.7, 5001,
updates table
S: 128.119.40.186, 80
D: 138.76.29.7, 5001
3
3: Reply arrives
dest. address:
138.76.29.7, 5001
4: NAT router
changes datagram
dest addr from
138.76.29.7, 5001 to 10.0.0.1, 3345

## Slide 15: NAT: Benefits
Local network uses just one (or a few) IP address as far as outside world is concerned
  No need to be allocated range of addresses from ISP
    16-bit port-number field: 60,000 simultaneous connections with a single LAN-side address!
    Might use a few IPs in a large private enterprise network
  Can change addresses of devices in local network without notifying outside world
  Can change ISP without changing addresses of devices in local network
Security
  Devices inside local net not explicitly addressable by outside world
  Connection needs to be initiated by inside device before a specific host can reach it from the public Internet

## Slide 16: NAT example use: load balancing
Load balancing
  Balance the load on a set of identical servers, which are accessible from a single IP address
NAT solution
  Servers are assigned private addresses
  NAT acts as a proxy for requests to the server from the public network
  NAT changes the destination IP address of arriving packets to one of the private addresses for a server
  Balances load on the servers by assigning addresses in a round-robin fashion
Notes: For most popular web sites, when you connect to an IP address it’s actually a load balancer with NAT-style functionality that balances load among various servers.

## Slide 17: NAT: Consequences
End-to-end connectivity broken
  NAT destroys universal end-to-end reachability of hosts on the Internet
  A host in the public Internet often cannot initiate communication to a host in a private network
  Even worse when two hosts that are in different private networks need to communicate with each other

## Slide 18: NAT: Consequences
Broken if IP address in application data
  Applications often carry IP addresses in the payload of the application data
  No longer work across a private-public network boundary
  Hack: Some NAT devices inspect the payload of widely used application layer protocols and, if an IP address is detected in the application-layer header or the application payload, translate the address according to the address translation table

## Slide 19: NAT: Consequences
Ossification of Internet protocols
  NAT must be aware of port numbers which are inside transport header
  Existing NATs don’t support your fancy new transport protocol
    and might even block standard protocols like UDP
  Result: Difficult to invent new transport protocols
    ...unless they just pretend to be TCP

## Slide 20: I/O systems

## Slide 21: Input and Output
A computer’s job is to process data
  Computation (CPU, cache, and memory)
  Move data into and out of a system (between I/O devices and memory)
Challenges with I/O devices
  Different categories: storage, networking, displays, etc.
  Large number of device drivers to support
  Device drivers run in kernel mode and can crash systems
Goals of the OS
  Provide a generic, consistent, convenient and reliable way to access I/O devices
  As device-independent as possible
  High performance I/O

## Slide 22: How does the CPU talk to devices?
Device controller: Hardware that enables devices to talk to the peripheral bus
Host adapter: Hardware that enables the computer to talk to the peripheral bus
Bus: Wires that transfer data between components inside computer
Device controller allows OS to specify simpler instructions to access data
Example: a disk controller
  Translates “access sector 23” to “move head reader 1.672725272 cm from edge of platter”
  Disk controller “advertises” disk parameters to OS, hides internal disk geometry
  Most modern hard drives have disk controller embedded as a chip on the physical device

## Slide 23: Review: Computer Architecture
Compute hardware
  CPU and caches
  Chipset
  Memory
I/O Hardware
  I/O bus or interconnect
  I/O controller or adaptor
  I/O device
Two types of I/O
  Programmed I/O (PIO)
    CPU does the work of moving data
  Direct Memory Access (DMA)
    CPU offloads the work of moving data to DMA controller

## Slide 24: Programmed Input Device
Device controller
  Status registers
    ready: tells if the host is done
    busy: tells if the controller is done
    int: interrupt
    …
  Data registers
A simple mouse design
  When moved, put (X, Y) in mouse’s device controller’s data registers
  Interrupt CPU
Input on an interrupt
  CPU saves state of currently-executing program
  Reads values in X, Y registers
  Sets ready bit
  Wakes up a process/thread or execute a piece of code to handle interrupt

## Slide 25: Programmed Output Device
Device
  Status registers (ready, busy, … )
  Data registers
Example
  A serial output device
Perform an output
  CPU: Poll the busy bit
  Writes the data to data register(s)
  Set ready bit
  Controller sets busy bit and transfers data
  Controller clears the busy bit
Notes:   Wait until ready bit is clear

## Slide 26: Direct Memory Access (DMA)
DMA controller or adaptor
  Status register (ready, busy, interrupt, …)
  DMA command register
  DMA register (address, size)
  DMA buffer
Host CPU initiates DMA
  Device driver call (kernel mode)
  Wait until DMA device is free
  Initiate a DMA transaction (command, memory address, size)
  Block
Controller performs DMA
  DMA data to device (size--; address++)
  Issue interrupt on completion (size == 0)
CPU’s interrupt handler
  Wakeup the blocked process

## Slide 27: Memory-mapped I/O
Use the same address bus to address both memory and I/O devices
  The memory and registers of I/O devices are mapped to address values
  Allows same CPU instructions to be used with regular memory and devices
I/O devices, memory controller, monitor address bus
  Each responds to addresses they own
Orthogonal to DMA
  May be used with, or without, DMA

## Slide 28: Polling- vs. Interrupt-driven I/O
Polling
  CPU issues I/O command
  CPU directly writes instructions into device’s registers
  CPU busy waits for completion
Interrupt-driven I/O
  CPU issues I/O command
  CPU directly writes instructions into device’s registers
  CPU continues operation until interrupt
Direct Memory Access (DMA)
  Typically done with Interrupt-driven I/O
  CPU asks DMA controller to perform device-to-memory transfer
  DMA issues I/O command and transfers new item into memory
  CPU module is interrupted after completion
Which is better, polling or interrupt-driven I/O?

## Slide 29: Polling- vs. Interrupt-driven I/O
Polling
  Expensive for large transfers
  Better for small, dedicated systems with infrequent I/O
Interrupt-driven
  Overcomes CPU busy waiting
  I/O module interrupts when ready: event driven

## Slide 30: How Interrupts are implemented
CPU hardware has an interrupt report line that the CPU tests after executing every instruction
  If a(ny) device raises an interrupt by setting interrupt report line
    CPU catches the interrupt and saves the state of current running process into PCB
    CPU dispatches/starts the interrupt handler
    Interrupt handler determines cause, services the device and clears the interrupt report line
Other uses of interrupts: exceptions
  Division by zero, wrong address
  System calls (software interrupts/signals, trap)
  Virtual memory paging

## Slide 31: I/O Software Stack
Kernel
User space

## Slide 32: Announcements
MPs, Take Two
  May resubmit, after MP7 due date and before final
  Half credit on resubmissions
  Watch Piazza later this week for grading and timing details
Talk today
  Scott Shenker (UC Berkeley)
  “Software-Defined Networking: Introduction and Retrospective”

## Slide 33: Interrupt Handling
Save context (registers that hw hasn’t saved, PSW etc)
Mask interrupts if needed
Set up a context for interrupt service
Set up a stack for interrupt service
Acknowledge interrupt controller, perhaps enable it
Save entire context to PCB
Run the interrupt service
Unmask interrupts if needed
Possibly change the priority of the process
Run the scheduler
Then OS will set up context for next process, load registers and PSW, start running process …

## Slide 34: Device Drivers
Manage the complexity and differences among specific types of devices (disk vs. mouse, different types of disks …)
Each handles one type of device or small class of them (eg SCSI)

## Slide 35: Typical Device Driver Design
Operating system and driver communication
  Commands and data between OS and device drivers
Driver and hardware communication
  Commands and data between driver and hardware
Driver responsibilities
  Initialize devices
  Interpreting commands from OS
  Schedule multiple outstanding requests
  Manage data transfers
  Accept and process interrupts
  Maintain the integrity of driver and kernel data structures

## Slide 36: Device Driver Behavior
Check input parameters for validity, and translate them to device specific language
Check if device is free (wait or block if not)
Issue commands to control device
  Write them into device controller’s registers
  Check after each if device is ready for next (wait or block if not)
Block or wait for controller to finish work
Check for errors, and pass data to device-independent software
Return status information
Process next queued request, or block waiting for next
Challenges:
  Must be reentrant (can be called by an interrupt while running)
  Handle hot-pluggable devices and device removal while running
  Complex and many of them; bugs in them can crash system

## Slide 37: Types of I/O Devices
Block devices
  Organize data in fixed-size blocks
  Transfers are in units of blocks
  Blocks have addresses and data are therefore addressable
  E.g. hard disks, USB disks, CD-ROMs
Character devices
  Delivers or accepts a stream of characters, no block structure
  Not addressable, no seeks
  Can read from stream or write to stream
  Printers, network interfaces, terminals
Like everything, not a perfect classification
  E.g. tape drives have blocks but not randomly accessed
  Clocks are I/O devices that just generate interrupts

## Slide 38: Char/Block Device Interfaces
Character device interface
  read( deviceNumber, bufferAddr, size )
    Reads “size” bytes from a byte stream device to “bufferAddr”
  write( deviceNumber, bufferAddr, size )
    Write “size” bytes from “bufferAddr” to a byte stream device
Block device interface
  read( deviceNumber, deviceAddr, bufferAddr )
    Transfer a block of data from “deviceAddr” to “bufferAddr”
  write( deviceNumber, deviceAddr, bufferAddr )
    Transfer a block of data from “bufferAddr” to “deviceAddr”
  seek( deviceNumber, deviceAddress )
    Move the head to the correct position
    Usually not necessary

## Slide 39: Sync vs Asynchronous I/O
Synchronous I/O
  read() or write() will block a user process until its completion
  OS overlaps synchronous I/O with another process
Asynchronous I/O
  read() or write() will not block a user process
  user process can do other things before I/O completion
  I/O completion will notify the user process

## Slide 40: Example: Blocked Read
A process issues a read call which executes a system call
System call code checks for correctness
If it needs to perform I/O, it will issues a device driver call
Device driver allocates a buffer for read and schedules I/O
Controller performs DMA data transfer
Block the current process and schedule a ready process
Device generates an interrupt on completion
Interrupt handler stores any data and notifies completion
Move data from kernel buffer to user buffer
Wakeup blocked process (make it ready)
User process continues when it is scheduled to run