## Slide 1: I/O systems
CS 241
April 30, 2014
University of Illinois

## Slide 2: Input and Output
A computer’s job is to process data
  Computation (CPU, cache, and memory)
  Move data into and out of a system (between I/O devices and memory)
Challenges with I/O devices
  Different categories: storage, networking, displays, etc.
  Large number of device drivers to support
  Device drivers run in kernel mode and can crash systems
Goals of the OS
  Provide a generic, consistent, convenient and reliable way to access I/O devices
  As device-independent as possible
  High performance I/O

## Slide 3: How does the CPU talk to devices?
Device controller: Hardware that enables devices to talk to the peripheral bus
Host adapter: Hardware that enables the computer to talk to the peripheral bus
Bus: Wires that transfer data between components inside computer
Device controller allows OS to specify simpler instructions to access data
Example: a disk controller
  Translates “access sector 23” to “move head reader 1.672725272 cm from edge of platter”
  Disk controller “advertises” disk parameters to OS, hides internal disk geometry
  Most modern hard drives have disk controller embedded as a chip on the physical device

## Slide 4: Review: Computer Architecture
Compute hardware
  CPU and caches
  Chipset
  Memory
I/O Hardware
  I/O bus or interconnect
  I/O controller or adaptor
  I/O device
Two types of I/O
  Programmed I/O (PIO)
    CPU does the work of moving data
  Direct Memory Access (DMA)
    CPU offloads the work of moving data to DMA controller

## Slide 5: Programmed Input Device
Device controller
  Status registers
    ready: tells if the host is done
    busy: tells if the controller is done
    int: interrupt
    …
  Data registers
A simple mouse design
  When moved, put (X, Y) in mouse’s device controller’s data registers
  Interrupt CPU
Input on an interrupt
  CPU saves state of currently-executing program
  Reads values in X, Y registers
  Sets ready bit
  Wakes up a process/thread or execute a piece of code to handle interrupt

## Slide 6: Programmed Output Device
Device
  Status registers (ready, busy, … )
  Data registers
Example
  A serial output device
Perform an output
  CPU: Poll the busy bit
  Writes the data to data register(s)
  Set ready bit
  Controller sets busy bit and transfers data
  Controller clears the busy bit
Notes:   Wait until ready bit is clear

## Slide 7: Direct Memory Access (DMA)
DMA controller or adaptor
  Status register (ready, busy, interrupt, …)
  DMA command register
  DMA register (address, size)
  DMA buffer
Host CPU initiates DMA
  Device driver call (kernel mode)
  Wait until DMA device is free
  Initiate a DMA transaction (command, memory address, size)
  Block
Controller performs DMA
  DMA data to device (size--; address++)
  Issue interrupt on completion (size == 0)
CPU’s interrupt handler
  Wakeup the blocked process

## Slide 8: Memory-mapped I/O
Use the same address bus to address both memory and I/O devices
  The memory and registers of I/O devices are mapped to address values
  Allows same CPU instructions to be used with regular memory and devices
I/O devices, memory controller, monitor address bus
  Each responds to addresses they own
Orthogonal to DMA
  May be used with, or without, DMA

## Slide 9: Polling- vs. Interrupt-driven I/O
Polling
  CPU issues I/O command
  CPU directly writes instructions into device’s registers
  CPU busy waits for completion
Interrupt-driven I/O
  CPU issues I/O command
  CPU directly writes instructions into device’s registers
  CPU continues operation until interrupt
Direct Memory Access (DMA)
  Typically done with Interrupt-driven I/O
  CPU asks DMA controller to perform device-to-memory transfer
  DMA issues I/O command and transfers new item into memory
  CPU module is interrupted after completion
Which is better, polling or interrupt-driven I/O?

## Slide 10: Polling- vs. Interrupt-driven I/O
Polling
  Expensive for large transfers
  Better for small, dedicated systems with infrequent I/O
Interrupt-driven
  Overcomes CPU busy waiting
  I/O module interrupts when ready: event driven

## Slide 11: How Interrupts are implemented
CPU hardware has an interrupt report line that the CPU tests after executing every instruction
  If a(ny) device raises an interrupt by setting interrupt report line
    CPU catches the interrupt and saves the state of current running process into PCB
    CPU dispatches/starts the interrupt handler
    Interrupt handler determines cause, services the device and clears the interrupt report line
Other uses of interrupts: exceptions
  Division by zero, wrong address
  System calls (software interrupts/signals, trap)
  Virtual memory paging

## Slide 12: I/O Software Stack
Kernel
User space

## Slide 13: Device drivers
Manage the complexity and differences among specific types of devices (disk vs. mouse, different types of disks …)
Special driver for each device type or group of them (eg, USB)

## Slide 14: Typical Device Driver Design
Operating system and driver communication
  Commands and data between OS and device drivers
Driver and hardware communication
  Commands and data between driver and hardware
Driver responsibilities
  Initialize devices
  Interpreting commands from OS
  Schedule multiple outstanding requests
  Accept and process interrupts
  Manage data transfers
Notes: Removed driver responsibility:
  * Maintain the integrity of driver and kernel data structures

## Slide 15: Device Driver Behavior
1. Check input parameters for validity, and translate them to device specific language
2. Check if device is free (wait or block if not)
3. Issue commands to control device
  Write them into device controller’s registers
  Check after each if device is ready for next (wait or block if not)
4. Block or wait for controller to finish work
5. Check for errors, and pass data to device-independent software
6. Return status information
7. Process next queued request, or block waiting for next
Challenges:
  Must be reentrant (can be called by an interrupt while running)
  Handle hot-pluggable devices and device removal while running
  Complex and many of them; bugs in them can crash system

## Slide 16: Types of I/O Devices
Block devices
  Organize data in fixed-size blocks
  Transfers are in units of blocks
  Blocks have addresses and data are therefore addressable
  E.g. hard disks, USB disks, CD-ROMs
Character devices
  Delivers or accepts a stream of characters, no block structure
  Not addressable, no seeks
  Can read from stream or write to stream
  Network interfaces, keyboards
Like everything, not a perfect classification
  E.g. tape drives have blocks but not randomly accessed
  Clocks are I/O devices that just generate interrupts

## Slide 17: Char/Block Device Interfaces
Character device interface
  read( deviceNumber, bufferAddr, size )
    Reads “size” bytes from a byte stream device to “bufferAddr”
  write( deviceNumber, bufferAddr, size )
    Write “size” bytes from “bufferAddr” to a byte stream device
Block device interface
  read( deviceNumber, deviceAddr, bufferAddr )
    Transfer a block of data from “deviceAddr” to “bufferAddr”
  write( deviceNumber, deviceAddr, bufferAddr )
    Transfer a block of data from “bufferAddr” to “deviceAddr”
  seek( deviceNumber, deviceAddress )
    Move the head to the correct position
    Usually optional

## Slide 18: User-level interfaces: syscalls
Character device interface
  read( deviceNumber, bufferAddr, size )
    Reads “size” bytes from a byte stream device to “bufferAddr”
  write( deviceNumber, bufferAddr, size )
    Write “size” bytes from “bufferAddr” to a byte stream device
Block device interface
  read( deviceNumber, deviceAddr, bufferAddr )
    Transfer a block of data from “deviceAddr” to “bufferAddr”
  write( deviceNumber, deviceAddr, bufferAddr )
    Transfer a block of data from “bufferAddr” to “deviceAddr”
  seek( deviceNumber, deviceAddress )
    Move the head to the correct position
    Usually not necessary

## Slide 19: Sync vs Asynchronous I/O
Synchronous I/O
  read() or write() will block a user process until its completion
  OS overlaps synchronous I/O with another process
Asynchronous I/O
  read() or write() will not block a user process
    returns -1, sets error code EAGAIN or EWOULDBLOCK
  user process can do other things before I/O completion
  can determine if device is ready with select() / poll() / epoll()
  Make asynchronous with O_NONBLOCK option on open() or later via fcntl()

## Slide 20: Finished our tour through the stack
Kernel
User space

## Slide 21: Example: Blocked Read
A process issues a read call which executes a system call
System call code checks for correctness
If it needs to perform I/O, it will issue a device driver call
Device driver allocates a buffer for read and schedules I/O
Controller performs DMA data transfer
Block the current process and schedule a ready process
Device generates an interrupt on completion
Interrupt handler stores any data and notifies completion
Move data from kernel buffer to user buffer
Wakeup blocked process (make it ready)
User process continues when it is scheduled to run

## Slide 22: Does I/O overhead matter?
Many steps involved in data I/O
How much can this overhead slow us down?
Experiment: copy.c
Notes: Also use this as a little review: Why does the program have a memory error when the buffer size is large?
(A: the buffer is allocated on the stack, not the heap via malloc(). Limited space on the stack. Switch to malloc and problem goes away.)

## Slide 23: Interrupt Handling
Save context (registers that hw hasn’t saved, PSW etc)
Mask interrupts if needed
Set up a context for interrupt service
Set up a stack for interrupt service
Acknowledge interrupt controller, perhaps enable it
Save entire context to PCB
Run the interrupt service
Unmask interrupts if needed
Possibly change the priority of the process
Run the scheduler
Then OS will set up context for next process, load registers and PSW, start running process …